## Slide 1: Solar-Powered Rover
By Team 66:
William Mancuso (EE), Bowen Williamson (EE), Margaret Burkes (EE), Keldon Ngo (EE), Kenny Bui (EE)
Project Sponsor: Dr. Xiangyu Meng
Faculty Advisor: Dr. Shahab Mehraeen
2/13/2025
#1
Prepared by: William Mancuso
Presented by: William Mancuso

## Slide 2: Functional Requirement #1: Convert Solar Energy to Power the Rover
Test #1: Ideal Condition Power Production
  Conducted by: Margaret Burkes & Keldon Ngo
  Test the power production of the panel throughout a sunny day
Test #2 : Non-Ideal Condition Power Production
  Conducted by: Keldon Ngo
  Test the power production throughout a cloudy day
Test #3 : Indoor Power Production
  Conducted by: Keldon Ngo
  Test the power production indoors.
2/13/2025
#2
Prepared by: Keldon Ngo
Presented by: Keldon Ngo

## Slide 3: Functional Requirement #2: Autonomously Switch Power Between Power Sources
Test #1: Battery charging from solar power
- Conducted by: Bowen Williamson
- Ensure battery charging while rover is stationary
Test #2: Monitor battery operation with solar power
- Conducted by: Bowen Williamson
- Time battery life during normal operation
- Compare current from charge controller vs. battery
2/13/2025
#3
Prepared by: Bowen Williamson
Presented by: Bowen Williamson

## Slide 4: Functional Requirement #3: Clean the Solar Panel
Test #1: Effectiveness of the Cleaning System
  Conducted by: Margaret Burkes
  Data Analysis: Taking the average of
2/13/2025
#4
Prepared by: Margaret Burkes
Presented by: Margaret Burkes

## Slide 5: Functional Requirement #3: Clean the Solar Panel
Test #2: Activation Of Brush Cleaning System
  Conducted by Kenny Bui
  Microcontroller acknowledges dust and debris, and different environmental aspects
  A pyranometer output and solar panel output power will be compared for decision
  Instrumentation: Recording device to visualize activation take place
  Protocol: Flour will be used to represent dust/debris, and different environmental scenarios can be provided to simulate false-positive triggers
2/13/2025
#5
Prepared by: Kenny Bui
Presented by: Kenny Bui

## Slide 6: Qualitative Specification #1: Compatibility with Existing Design
Terrain Test
  Conducted by: Margaret Burkes
  Previous Team’s Results with 36kg of additional weight:
2/13/2025
#6
Terrain: | Speed:
Sand | 0.5 m/s
Grass | 0.5 m/s
Concrete | 0.62 m/s
Levee | 0.33 m/s
Prepared by: Margaret Burkes
Presented by: Margaret Burkes

## Slide 7: Qualitative Specification #3: Portability
Assembly Test
  -Conducted by: William Mancuso
  -Measure assembly and disassembly time
  -Test equipment: Drill or Screwdriver
  -Measure and compare final dimensions
2/13/2025
#7
Prepared by: William Mancuso
Presented by: William Mancuso

## Slide 8: Environmental Impact Assessment
• Decrease in power required from the grid
• Recyclable components
• Emission-free operation
Testing with biodegradable materials (flour)
Dry cleaning; no harmful chemicals
2/13/2025
#8
Prepared by: Bowen Williamson
Presented by: Bowen Williamson

## Slide 9: Safety Assessment
2/13/2025
#9
Concern | Safety Preventative
Electrical Shock Hazard | All electrical connections on our rover are properly grounded to prevent shock hazard.
Arc Flash Hazard | All electrical connections are covered and have appropriate safety measures in place to avoid short circuiting. This will mitigate arc flashes.
Overcurrent | All major electrical components have incorporated fused connections that are sized properly and are expected to pop in the case of overcurrent.
Moving object hazard with motors on cleaning system | There is a cancel button designed in the brush cleaning system that is designed to cancel all operation of the cleaning system in case it is needed.
Unexpected cleaning system activation | There is also a buzzer designed to trigger before the cleaning system is activated to alert all nearby prior to the cleaning system activating.
Kill Switch | There are two switches attached to the battery that can be quickly disengaged to de-energize the entire rover in the case that it is needed
Prepared by: Kenny Bui
Presented by: Kenny Bui

## Slide 10: Appendix
Measurable Specification #1: Budget
Measurable Specification #2: Interior Space
Measurable Specification #3: Weight Limit
Qualitative Specification #2: Weatherproof Design
2/13/2025
#10

## Slide 11: Measurable Specification #3: Weight Limit
Max Speed Test
  Conducted by: William Mancuso
  Measure the speed of the fully assembled rover
  Test equipment stop-watch, tape measure, camera
  Compare speeds
2/13/2025
#11
Prepared by: William Mancuso
Presented by: William Mancuso

## Slide 12: Qualitative Specification #2: Weatherproof Design
Ducky Assumption
  The assumption made by the team will be that the Ducky Products spray is reputable
  The treated electronics will be water-proof
2/13/2025
#12
Prepared by: Keldon Ngo
Presented by: Keldon Ngo

## Slide 13: Measurable Specification #2: Interior Space
Test: Chassis Measurement
  Conducted by Kenny Bui
  Measure overall interior space of the chassis
  Measure and analyze volumes of components within the chassis
  Calculate the occupied space within the chassis
  Instrumentation: Tape Measure and Spec Sheets
  Overall Interior Space – Occupied Interior Space = Remaining Interior Space
2/13/2025
#13
Prepared by: Kenny Bui
Presented by: Kenny Bui

## Slide 14: Measurable Specification #1: Budget
1/21/2025
#14
Project Funding: $4,000
Total Spent: $1,549.69
Remaining: $2,450.31
Prepared by: Bowen Williamson
Presented by: Bowen Williamson