## Slide 1: Solar-Powered Rover
By Team 66:
William Mancuso (EE), Bowen Williamson (EE), Margaret Burkes (EE), Keldon Ngo (EE), Kenny Bui (EE)
Project Sponsor: Dr. Xiangyu Meng
Faculty Advisor: Shahab Mehraeen
10/2/2024
#1

## Slide 2: Objective Statement
The main objective of this project is enhancing the previously built rover, which is battery powered, by integrating solar power, autonomous power switching between solar and battery power, and an independent cleaning system for the solar panel.
10/2/2024
#2

## Slide 3: Functional Requirements
# | Weight | Function | Explanation
F1 | 0.4 | Convert solar energy to power the rover. | Utilize solar panels to absorb sunlight as an additional power source to the battery power.
F2 | 0.35 | Autonomously switch power between power sources. | Autonomously switch between battery and solar power.
F3 | 0.25 | Clean the solar panels. | Intermittently clean off debris from solar panel to maximize energy absorption and efficiency.
10/2/2024
#3

## Slide 4: Qualitative Constraints
# | Weight | Qualitative Constraint | Explanation
Q1 | 0.40 | Compatibility with Existing Design | Make sure that the new implementations to the previous rover are compliant with each other. The additions should merge with the existing design seamlessly.
Q2 | 0.35 | Weatherproof Design | The solar panel system should be built to withstand the elements of Louisiana such as wind, precipitation, and heat.
Q3 | 0.25 | Portability | Make sure that the system doesn’t hinder the transportation of the rover. Should be convenient to maneuver without disassembly.
10/2/2024
#4

## Slide 5: Quantitative Constraints
# | Weight | Name | Symbol | Units | Value(s) | Explanation
M1 | 0.5 | Budget | B | $ | 4000 | A budget of $4000 was decided upon by the sponsor.
M2 | 0.4 | Interior Space | S | M^3 | 0.977 | This is the amount of available space inside the rover’s chassis to install new electronic components.
M3 | 0.1 | Weight Limit | W | Kg | <36.3 | The max additional weight load was measured at 36.3kg. The team would like to stay under this variable.
10/2/2024
#5

## Slide 6: Function Objective Tree
10/2/2024
#6
Autonomously Switch Power Sources
Clean Solar Panels
Generate Solar Power
Detect Power Output Loss
Recognize Power Generation Loss
Absorb Solar Energy
Execute Pre-Programming For Action
Activate Brush Cleaning System
Convert Solar Rays to Electricity
Switch to Alternative Power Source
Clear debris off solar panel surface
Supply Power to Rover System and Battery

## Slide 7: Concept Generation:
10/2/2024
#7
 | Self-Cleaning | Autonomous Power Switching | Solar Panel
Concepts | Continued on the next slides. | Voltage Regulator with Arduino, DC/DC Converter w/ Arduino, Solar Charge Controller | Monocrystalline, Polycrystalline, Thin-Film

## Slide 8: Concept Evaluation & Selection: Self-Cleaning
10/2/2024
#8
 |  | Concepts |  | 
Criterion | Weights | Air Compressor | Electrostatic Method | Brush Method
Cost | 30 | 0 | -1 | 1
Cleans Effectively | 25 | -1 | 1 | 0
Mass | 20 | -1 | 0 | 1
Non-abrasive | 20 | 0 | 1 | -1
Maintenance | 5 | -1 | 1 | 0
Weighted Total | 100 | -0.5 | 0.2 | 0.3

## Slide 9: Concept Evaluation & Selection: Solar Panel
10/2/2024
#9
 |  | Concepts |  | 
Criterion | Weights | Thin Film | Polycrystalline | Monocrystalline
Efficiency | 40 | -1 | 0 | 1
Cost | 25 | 1 | 0 | -1
Weight | 20 | 1 | -1 | -1
Life-span | 15 | -1 | 1 | 1
Weighted Total | 100 | -.1 | -.05 | 0.1

## Slide 10: Concept Evaluation & Selection: Autonomous Power Switching
 |  | Concepts |  | 
Criterion | Weights | Voltage Regulator with Arduino | DC/DC Converter with Arduino | Solar Charge Controller
Functional Accuracy | 45 | -1 | 0 | 1
Simplicity | 25 | 0 | -1 | 1
Programmability | 20 | -1 | 0 | 1
Cost | 10 | 1 | 0 | -1
Weighted Total | 100 | -0.55 | -0.25 | 0.8
10/2/2024
#10

## Slide 11: Concept Selection:
10/2/2024
 | Solar Panel Cleaning System | Autonomously Switch Battery | Solar Panel
Concepts | Brush Method | Solar Charge Controller | Monocrystalline
#11

## Slide 12: Preliminary System Description
10/2/2024
#12
36V Battery
Solar Panel
PWM Solar Charge Controller
Bus Bars
Sources
To Rover
Source Management
Distribution
Solar Panel Cleaning System

## Slide 13: Preliminary Budget
10/2/2024
#13
PWM Charge Controller | $250
Solar Panel | $2,000
Arduino | $50
Cleaning System | $400
Wiring | $100
Total Cost | $2,800
Project Budget | $4,000

## Slide 14: Preliminary Schedule/Timeline
10/2/2024
#14

## Slide 15: Preliminary Schedule/Timeline
10/2/2024
#15

## Slide 16: Appendices
10/2/2024
#16

## Slide 17: Pros and Cons of the Self-Cleaning Systems
10/2/2024
#17
 | Air Compressor | Electrostatic Method | Brush
Pros | Less likely to scratch | Requires humidity No scratch 90% effective | Easily obtainable parts Within budget Low power consumption
Cons | Weight distribution Large power consumption | Too expensive May not clean heavier debris | May scratch May trap debris

## Slide 18: Pros and Cons of the Solar Panels:
10/2/2024
 | Monocrystalline | Polycrystalline | Thin-Film
Pros | High Efficiency: 20-23% Space-Saving Longer Lifespan | Good Efficiency Cost-Effective Decent Space Utilization | Lightweight and Flexible Performance in High Temperatures Lower Cost
Cons | Expensive Production | Space Shorter Life-span Less efficient | Low Efficiency: 13-15% Consume lots of space Not Durable
#18

## Slide 19: Pros and Cons of the Autonomous Battery Switching:
 | Voltage Regulator w/ Arduino | DC/DC Converter w/ Arduino | Solar Charge Controller
Pros | Low cost | Low cost | Easily Programmable No design needed
Cons | Too simple to accomplish the task | Would have to be designed for our specific parameters. Would have to code our own program. | Most expensive
10/2/2024
#19
Notes: In order to autonomously switch between solar power and battery power, the main thing we thought to use was a solar charge controller. Charge controllers are essentially controllable buck converters.

## Slide 20: Evaluation and Selection : Autonomous Battery Switching
Solar Panel
Battery
Solar Charge Controller
LOUIS
10/2/2024
#20

## Slide 21: Overview of Self-Cleaning:
10/2/2024
#21
Key:
Brush
Rails

## Slide 22: Drawings of Self-Cleaning Systems:
10/2/2024
Air Compressor
Electrostatic Method
Brush Method
#22

## Slide 23: Appendices: HOQ
10/2/2024
House of Quality:
#23

## Slide 24: References:
10/2/2024
#24
“Do Solar Panels Have Mounting Holes in Back.” Solar Industry Watch, 29 Aug. 2024, solarindustrywatch.org/do-solar-panels-have-mounting-holes-in-back/.
“Do Solar Panels Have Mounting Holes in the Back?” Sungoldsolar, 12 Sept. 2024, www.sungoldsolar.us/do-solar-panels-have-mounting-holes-in-the-back/.
Ecoppa. “ECOPPIA’s E4 Robotic Cleaning Solution.” ECOPPIA’S E4 ROBOTIC CLEANING SOLUTION, www.ecoppia.com/warehouse/temp/ecoppia/E4_Product_Overview.pdf. Accessed 23 Sept. 2024.
Levitan, Dave. “Tech from Mars: Self-Cleaning Solar Panels.” IEEE Spectrum, IEEE Spectrum, 13 July 2024.
Meng, Xiangyu. “Rover: LOUIS.” YouTube, YouTube, 18 May 2024, www.youtube.com/watch?v=Htv0q-P5DVE&t=1s.
“Maximizing Solar Efficiency: Nano Coatings for Solar Panels.” Nasiol, 1 July 2024.
Mazumder, M.K., et al. “Electrostatic Removal of Particles and Its Applications to Self-Cleaning Solar Panels and Solar Concentrators.” Developments in Surface Contamination and Cleaning, William Andrew Publishing, 29 Mar. 2011.
“Spirit Rover (MER-A) - NASA - NSSDCA - Spacecraft - Details.” Nasa, 2003, nssdc.gsfc.nasa.gov/nmc/spacecraft/display.action?id=2003-027A.